## Slide 1
Zynq UltraScale+ MPSoC bring up
and Latencies in VCU
Vijay Vanga

## Slide 2
1.Petalinux
1.1 Packages download.
1.2 Image building process for zynq board.
2.Zynq UltraScale+ MPSoC
2.1 Board bring up activities.
3.Latency in VCU
3.1 Different types of latency in vcu
3.2 Latency debugging
Content:
27 Dec, 2023
2
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 3
Petalinux is used to generate the binaries for various xilinx FPGA(media type)boards by using some files .
Steps to generate binaries for zynq ultrascale +MPSoC board:
1.first download petalinux source code from www.xilinx.com petalinux
Latest version.
2.Download vuc and bsp from same site with same version.
3.make petalinux file as executable
$chmod 777 petalinux-v2023.1-05012318-installer.run
$./ petalinux-v2023.1-05012318-installer.run
$source ./settings.sh
$sudo dpkg -reconfigure dash
$echo $PETALINUX
petalinux:
27 Dec, 2023
3
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 4
$petalinux-create -t project -s <path of bsp>
$cd xilinx-vcu-zcu106-v2023.1-final.bsp
$petalinux-config
$petalinux-config –get-hw-description=<path of the enable hardware with file.xsa file name>
$petalinux-build
After completion of compilation process it generates some files ie,Image,BOOT.BIN,system.dtb,boot.src and rootfs.tar.gz in newly create project images directory and build.log in build directory.
petalinux:
27 Dec, 2023
4
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 5
There are different types of board available ie zcu102,zcu104,zcu106
Steps to Board bring up of zynq ultrascale +MPSoC:
SD card partition:
Make partions the sd card and copy the booting file in the sd card card
Format the sd card by make partions:
a)By command lines:
$lsblk or $fdisk -l(to identify media /dev/sdx)
$sudo fdisk /dev/sdx(which gives options to modify any partition and get information)
$Sudo parted /dev/sdx(entering into sd card)
$mklabel gpt(if you want to create new partition table)
$mkpart primary [file system type ex,ext4,fat32] [start ie,1MB,100%]
[end ie,100%,mb](creating partition)
Zynq UltraScale+ MPSoC bring up:
27 Dec, 2023
5
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 6
$name [partition name] [name]
$quit
$ sudo mkfs.vfat /dev/sdx1(sdx1—replace with partition device name)
b)GUI partition of sd card.
Copy (boot.src, BOOT.BIN, Image, system.dtb, rootfs.cpio. gz.uboot) into boot partition ie FAT format.
Sd card partition:
27 Dec, 2023
6
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 7
Commands for Zynq ultrascale+ mpsoc:
$ssh xxxx@000.000.000.000(ip address to connect)
Password:xxxxxx
Login into board:
$minicom -WD /dev/ttyUSBX
$ps aux | grep USBX(if USB is locked )
$sudo su
$dmesg | grep bound (to know dp port id )
$modetest -M xlnx(to see whole connector id’s)
Zynq UltraScale+ MPSoc:
27 Dec, 2023
7
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 8
1.The vcu h.264/h.265 is supports of 3480x2160 pixels at 60Hz while encodeing and decoding simultaneously.
2.vcu supports AVC and HECV standards.
3.The vcu contains programmable logic(PL)and processing system(PS) and also it requires interfaces(AXI) to transfer data ti various units.
Latency in pipeline:
In pipeline data passes through various blocks in this occurs same delay by passing from one structural block to another structural block.
Causes of latencies occur in pipeline:
a. Buffer to Buffer data transfer.
b. while passing data receiver buffer needs memory allocation.
Latency in VCU H.264/H.265:
27 Dec, 2023
8
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 9
Different types of latencies in pipeline:
1. Normal-Latency:All possible frame types (I, P, and B) are supported and there is no restriction on GOP structure. This are occurred by internal buffers.
2.No Reordering (Reduced-Latency): The VCU encoder works at framelevel. Hardware rate control is used to reduce the bitrate variations. I-only, IPPP, and low-delay-P are supported. There is no output reordering.
3.Low-Latency:The frame is divided into multiple slices.The VCU encoder generates a slice done interrupt at every end of the slice .
4.xilinx Low-Latency: The producer (Capture DMA) and the consumer (VCU encoder) work on the same input buffer concurrently but consumer can access the only read whenever producer completed write opertion then consumer access.
Latencies in pipeline:
27 Dec, 2023
9
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 10
Latencies in pipeline:
27 Dec, 2023
10
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 11
4x 1080p60 AVC NV12 Xilinx Low-Latency Pipeline:
gst-launch-1.0 -v v4l2src io-mode=dmabuf device=/dev/video0 ! video/x-raw/(memory:XLNXLL/), width=1920, height=1080, format=NV12, framerate=60/1 !queue ! omxh264enc control-rate=low-latency target-bitrate=6000 prefetch-buffer=TRUE num-slices=8 periodicity-idr=240 cpb-size=500 initial-delay=250 gdr-mode=horizontal gop-mode=low-delay-p ! video/x-h264,alignment=nal ! queue max-size-buffers=0 ! omxh264dec low-latency=1 !video/x-raw/(memory:XLNXLL/) ! queue max-size-bytes=0 ! fpsdisplaysinkname=fpssink text-overlay=false 'video-sink=kmssink bus-id=a00c0000.v_mix plane-id=30 hold-extra-sample=1 show-preroll=false sync=true' sync=true -v
$GST_DEBUG=
"basesink:5" GST_DEBUG_FILE="/runreported_serial_4k_avc.txt"
Example pipeline:
27 Dec, 2023
11
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 12
To check reported latency:
$grep -inr "latency set" serial_4k_avc.txt
To check instantaneous latency:
$GST_DEBUG="GST_TRACER:7" GST_TRACERS=latency GST_DEBUG_FILE="/run/instantaneous_latency_serial_4k_avc.txt"
Gst-launch-1.0 <pipeline>
Latency debugging:
27 Dec, 2023
12
© Copyright Softnautics (a MosChip Company), Confidential

## Slide 13
June 12, 2023
© Copyright Softnautics (a MosChip Company), Confidential